## Slide 1: Glockenspiel — Tuned Metal-Bar Idiophone Build Packet
Musical instrument documentation capstone
Build packet: glockenspiel
Generated: 2026-05-08

## Slide 2: Project Intent
Build a 25-bar chromatic C5-C7 glockenspiel from the existing workbook design table, with a parallel 10-bar C-major-pentatonic art-fair variant sharing the same aluminum stock and frame jig.
6061-T6 aluminum bars (0.25 in × 1.00 in flat stock) on a CNC-routed Black Walnut frame.
Free-free beam acoustics, no arch undercut, no resonator tubes.
Cord-through-node-holes mounting with rubber grommets and 1/8 in stainless support rods.
All published lengths are first-pass cut-long targets; effective K is recalibrated from a C5/A5/C7 pilot.
Speaker notes: Read design.md before committing to dimensions or sourcing decisions. The K-calibration pilot is non-optional.

## Slide 3: Physics Model
Free-Free Beam (Metal)
lambda_1 = 4.730 f_1 = (lambda_1^2 / (2*pi*L^2)) * sqrt(E*I/(rho*A))
f ~= K * t / L^2 L ~= sqrt(K * t / f)
material = 6061-T6 Aluminum K = 204431 (imperial: t and L in inches, f in Hz) t = 0.250 in w = 1.000 in
K_metal = (4.730^2 / (2*pi)) * sqrt(E / (12*rho)) / 0.0254 node_1 = 0.2242 * L node_2 = 0.7758 * L
Speaker notes: Width does NOT affect frequency. Per references/acoustic-models.md, NAF K2 corrections, vessel Helmholtz corrections, and cantilever wood K-tables do NOT apply. The honest correction loop is per-lot K calibration from pilot measurements.

## Slide 4: Material Decision Matrix
6061-T6 Aluminum (default): K=204431, bright bell-like, long sustain, lowest cost.
Brass C260: K=145325, warm classic glock tone, premium cost.
Steel 1018: K=204267 (similar to Al), harsh and very loud.
304 Stainless: K=198770, clean modern tone, weather-resistant.
Phosphor Bronze: K=142593, richest sustain, highest cost.
To switch metals: replace K in family-spec.csv and recompute predicted_length_in = sqrt(K*t/f).
Speaker notes: Aluminum and Steel have nearly identical K because the E/rho ratio is similar; the practical difference is mass and timbre, not length.

## Slide 5: Bar Schedule (chromatic + pentatonic)
25 chromatic bars C5-C7 (full schedule in family-spec.csv).
10 pentatonic bars (C5,D5,E5,G5,A5,C6,D6,E6,G6,A6) — art-fair “no wrong notes” variant.
Note | MIDI | Target Hz | Length in | Node 1 in | Node 2 in
C5 | 72 | 523.251 | 9.883 | 2.216 | 7.667
A5 | 81 | 880.000 | 7.621 | 1.709 | 5.912
C6 | 84 | 1046.502 | 6.988 | 1.567 | 5.422
A6 | 93 | 1760.000 | 5.389 | 1.208 | 4.181
C7 | 96 | 2093.005 | 4.941 | 1.108 | 3.834

## Slide 6
Speaker notes: Lengths assume K = 204431. Always cut at predicted + 0.25 in trim allowance. K_eff is calibrated from pilot bars before the full run.

## Slide 7: Mounting And Frame
Piano-keyboard layout: naturals (15) front row, sharps/flats (10) back row raised 0.5 in.
Each bar drilled with 3/16 in node holes; cord captures the bar at both nodes.
Rubber grommets seat in CNC-routed walnut pockets; durometer (Shore 30A/50A/70A) chosen via pilot.
1/8 in stainless rod runs full row length as backup restraint (must NOT contact bar).
Frame envelope: 33.25 in (chromatic) or 14.50 in (pentatonic) wide × ~12 in deep.
Speaker notes: Mounting damping is the structural risk that dominates sustain. See risks.md.

## Slide 8: Hardware Alignment
Bar marking & cutting: bench-top (chop saw + stop-block sled).
Node hole drilling: drill press + V-block jig + hardwood backer.
Bar tuning: belt sander or fine bench file, symmetric trim.
Frame routing: CNC router (the only true CNC operation in this build).
Mounting: cord + grommet + stainless rod, all bench-top.
Validation: chromatic tuner (>= 2 kHz), microphone for sustain logging.
Speaker notes: The frame is the only CNC step. Everything else is bench-top with simple jigs from jig-decision.md.

## Slide 9: How To Use This Packet
Start with design.md for intent and assumptions.
Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
Use drawing-brief.md, drawings/, cad/, and cnc/ before machining.
Use jig-decision.md as the shop stop/go sheet.
Use validation.csv as the K-calibration and tuning log.
Print the packet for shopping, shop work, and validation.

## Slide 10: File Map
design.md: Project intent, governing model, material decision matrix, mounting strategy, validation plan.
family-spec.csv: 25 chromatic + 10 pentatonic bar dimensions.
bom.csv: Bar set + frame + hardware + mallets + tooling + measurement gear.
sourcing.csv: Supplier candidates with all prices marked “not verified”.
cut-list.csv: Bar stock, walnut frame stock, jig material.
validation.csv: prebuild rows for all 35 bars + per-stage rows (flat_bar/post_trim/mounted/framed) for C5/A5/C7 pilots.
assembly-manual.md: Pilot-first build philosophy and full bench workflow.
supplier-rfq.md: RFQ template covering aluminum + alternates + walnut + hardware + tooling.
drawing-brief.md: Five drawing classes with tolerances.
visual-bom-brief.md: Image-forward BOM plate spec.
risks.md: Acoustic / structural / ergonomic / supply / fit-finish risk register.
photo-shotlist.md: Build-log photo plan.
resources.md: Provenance, family context, public-safety inventory.
jig-decision.md: Pilot fixture decisions and release gates.
drawings/: Per-pilot bar SVGs, family-overview, frame-layout, mounting-detail, visual-bom-plate.
cad/: OpenSCAD master + SolidWorks contract (CSV + plan).
cnc/: cnc-plan.json, operations.csv, setup-sheet.md (frame-routing focus).
jigs/: Pilot fixture artifacts as built.
wolfram/: instrument-model.wl with kMetal/lBar/Manipulate/validation plot.
site/: Build-log static site.

## Slide 11: Family Spec
Note | MIDI | Hz | L in | Node 1 | Node 2
C5 | 72 | 523.251 | 9.883 | 2.216 | 7.667
C#5 | 73 | 554.365 | 9.602 | 2.153 | 7.449
D5 | 74 | 587.330 | 9.328 | 2.091 | 7.237
E5 | 76 | 659.255 | 8.805 | 1.974 | 6.831
G5 | 79 | 783.991 | 8.074 | 1.810 | 6.264
A5 | 81 | 880.000 | 7.621 | 1.709 | 5.912
C6 | 84 | 1046.502 | 6.988 | 1.567 | 5.422
E6 | 88 | 1318.510 | 6.226 | 1.396 | 4.830
A6 | 93 | 1760.000 | 5.389 | 1.208 | 4.181
C7 | 96 | 2093.005 | 4.941 | 1.108 | 3.834

## Slide 12
Speaker notes: Full 25-bar schedule plus 10-bar pentatonic block in family-spec.csv. All values first-pass; pilot K calibration corrects them.

## Slide 13: Build Workflow
Receive aluminum stock and verify dimensions.
Mark bar lengths and node positions per family-spec.csv.
Cut bars to length (cut long by 0.25 in).
Drill node holes on drill press with V-block jig.
Strike-test pilot bars (C5/A5/C7) on foam supports; calibrate K_eff.
Trim to pitch with symmetric end removal.
CNC-route walnut frame rails and grommet pockets.
Run mounting prototype rig with three durometer grommets.
Assemble frame and mount all bars.
Final validation: every bar within +/- 5 cents at soft dynamic.

## Slide 14: Sourcing And BOM
Primary metal: 6061-T6 Aluminum 1/4” × 1” flat bar (~18 ft for chromatic + pentatonic + scrap).
Frame: Black Walnut 4/4 dressed to 3/4” thick (about 6 board feet).
Hardware: paracord, three durometer grommets, 1/8” stainless rod, rubber feet, fasteners.
Mallets: hard rubber (default) + brass (orchestral upgrade) + optional lexan/Delrin.
Tooling: 1/4” downcut + 1/8” upcut router bits, 3/16” drill bit, 80T non-ferrous chop-saw blade.
Measurement: chromatic tuner with 2 kHz+ range (Peterson StroboClip HD).
All sourcing.csv prices marked “not verified” — verify before purchase.

## Slide 15: Shop Packet
cut-list.csv for stock planning.
assembly-manual.md for away-from-keyboard work.
validation.csv for measured Hz, cents error, sustain, timbre.
Pilot gate: don’t cut all 25 bars until C5/A5/C7 pass flat_bar, post_trim, mounted, framed.

## Slide 16: Drawings, CAD, CNC
drawing-brief.md defines required views and tolerances.
drawings/ has three pilot bar SVGs + family-overview + frame-layout + mounting-detail + visual-bom-plate.
cad/ has OpenSCAD master + SolidWorks contract (CSV + plan).
cnc/ has the frame-routing operation graph (no bar CNC).
jigs/ collects pilot fixture artifacts.
drawing

## Slide 17
drawing drawing drawing drawing drawing drawing

## Slide 18: Validation Plan
Pilot: cut C5, A5, C7 cut-long; mass-and-strike test; compute K_eff = f * L^2 / t.
If pilot K_eff differs from workbook K by more than 5%, update family-spec.csv and workbook B21 before cutting remaining bars.
Trim each bar to within +/- 10 cents (pilots) or +/- 5 cents (production) by symmetric end removal.
Mount on prototype rig with three durometer grommets; pick the one that preserves >= 75% of flat-bar sustain.
Mount all bars on walnut frame; run final framed validation row.
Cents error: cents = 1200 * log2(measured_hz / target_hz).

## Slide 19: Open Risks / Decisions
Aluminum mill-lot K variance can shift pitch 5-10%; pilot calibrates per lot.
Grommet durometer dominates sustain; pilot Shore 30A/50A/70A before standardizing.
Striker hardness (brass / hard rubber / lexan) shifts timbre dramatically; ship at least two pairs.
Frame ergonomics (bar reach, accidental row offset, transport) need full-size taped layout.
Clear-coat finish on aluminum can shift pitch 3-10 cents flat; tune after finish or leave raw.
Workbook K constants (B16-B20) are first-pass; recalibrate per lot from pilot data.

## Slide 20: Next Actions
Cut C5/A5/C7 pilot bars and measure K_eff.
Pilot the three durometer grommets; pick one and record decision.
CNC-route the walnut frame after K and durometer are confirmed.
Cut the remaining 22 chromatic bars (or 7 pentatonic) using calibrated K.
Assemble, validate, photograph, and update validation.csv.
Replace TBDs with measured/source-backed values.
Verify live supplier prices and availability before buying.